## Slide 1
Transferable Neural WAN TE
for Changing Topologies
Abd AlRhman AlQiam1, Yuanjun Yao2, Zhaodong Wang2, Satyajeet Singh Ahuja2, Ying Zhang2, Sanjay G. Rao1, Bruno Ribeiro1, Mohit Tawarmalani1
1
2

## Slide 2
Traditional Traffic Engineering Pipeline
Input TMs
Centralized
SDN Controller
Has a global view of the network
optimizes a network-wide objective (e.g., minimize link utilization)
It employs linear programming to route traffic
Route traffic
45%
55%
Capacities + Tunnels
EBB Controller
SWAN, B4,
1
2
3
4
5
C1
C1
C2
C2
C3
C3

## Slide 3
Traditional Traffic Engineering Pipeline
Input TMs
LP Solver
Route traffic
45%
55%
Capacities + Tunnels
Issues with this approach:
Input TMs don't fully capture actual TM (e.g., prediction error)
  LP solvers can’t cope with prediction inaccuracies
  Resulting in suboptimal routing
LP solvers do not scale to large topologies
1
2
3
4
5
C1
C1
C2
C2
C3
C3

## Slide 4
Traditional Traffic Engineering Pipeline
Input TMs
LP Solver
Route traffic
45%
55%
Capacities + Tunnels
Neural Model
Why ML-based TE?
DOTE, NSDI 23
TEAL, SIGCOMM 23
1
2
3
4
5
C1
C1
C2
C2
C3
C3
Issues with this approach:
Input TMs don't fully capture actual TM (e.g., prediction error)
  LP solvers can’t cope with prediction inaccuracies
  Resulting in suboptimal routing
LP solvers do not scale to large topologies

## Slide 5
Why ML-based TE?
Input TMs
LP Solver
Route traffic
45%
55%
Capacities + Tunnels
Neural Model
DOTE, NSDI 23
TEAL, SIGCOMM 23
1
2
3
4
5
C1
C1
C2
C2
C3
C3
Can compensate for prediction error
Results in a better routing
30%
70%
Faster
Scale to large topologies

## Slide 6
Challenges for ML-based TE
Networks evolve continuously
  Organic growth
  Maintenance
  Failures
Existing neural TE schemes
  Focus on fixed topologies and fixed set of tunnels
  Do not generalize to topologies outside training set

## Slide 7
Contributions
HARP: First neural TE scheme that can handle changing topologies
HARP is transferable across topologies
  Preserves key invariances to natural inputs transformations (e.g., reordering tunnels)
  Neural architecture is aligned to the optimization model
HARP outperforms classical LP solvers:
  5-13% lower average Maximum Link Utilization (MLU) based on traffic matrix predictor
  100x faster on large topologies
HARP performs well even with topologies/failures outside training data
  Close to optimal MLU in all cases
  34% lower MLU than DOTE and TEAL on average

## Slide 8
Fixed
size TMs
DOTE
Routing on fixed set of tunnels
DOTE (NSDI 23)
  Fully connected neural network
  Does not model capacities, tunnels..
Why explicitly modeling topology is important?
Model cannot distinguish two scenarios where tunnels and capacities vary
1
2
3
4
5
30%
70%
C1
C1
C2
C2
C3
C3
1
2
3
4
5
30%
70%
C1
C1
C2
C2
C3
C3
For the same input TMs, DOTE generates the same routing regardless of tunnels and capacities
C3 > C1 > C2

## Slide 9
Why preserving invariances is important?
Identical topologies except tunnel relabeling
Existing neural models do not guarantee identical routing in the two scenarios
Prerequisite to generalize to topologies unseen in training
1
2
3
4
5
30%
70%
#2
#1
C1
C1
C2
C2
C3
C3
1
2
3
4
5
30%
70%
#1
#2
C1
C1
C2
C2
C3
C3

## Slide 10
HARP Design Principles
Principle 1: Ensure invariances to input transformations
  Node relabeling
  Tunnel relabeling
  Traffic matrix transpose
Principle 2: Aligning neural architecture to optimization model
  Mimics the iterative nature of optimization algorithms
  An example of the power of neural algorithmic reasoning*
Allow HARP to generalize to topologies beyond training.
* Beatrice Bevilacqua, Kyriacos Nikiforou, Borja Ibarz, Ioana Bica, Michela Paganini, Charles Blundell, Jovana Mitrovic, and Petar Veličković. Neural algorithmic reasoning with causal regularisation. ICML, 2023

## Slide 11
1) Model Topology
And
Capacities
2) Model Tunnels
3) Initial Routing Predictor
4) Iteratively improve the routing
HARP Overview
Topology
and
Capacities
GNN
Set
Transformer
Tunnels described as sets of edges
Tunnel Embeddings
Modeling tunnels as sets of edges introduces an invariance to traffic matrix transpose
HARP Design

## Slide 12
1) Model Topology
And
Capacities
2) Model Tunnels
HARP Design
Tunnel Embeddings
3) Initial Routing Predictor

## Slide 13
1) Model Topology
And
Capacities
2) Model Tunnels
HARP Design
Tunnel Embeddings
3) Initial Routing Predictor
Input TMs
MLP
Initial Routing
4) Iteratively improve the routing
RAU
Final
Routing
RAU: Recurrent Adjustment Unit, applied K times
Network-wide MLU
Highest link utilization in a tunnel
RAU

## Slide 14
Experimental Setup
Datasets:
  AnonNet: Data collected from real cloud WAN
  GEANT: Public dataset
  Abilene: Public dataset
  KDL: Synthetic TMs
Baselines:
  DOTE
  TEAL
  Gurobi (widely-used LP solver)
Schemes evaluated using ground-truth matrix unless otherwise mentioned

## Slide 15
Topology changes in real-world cloud WAN
Topology and TM at 1 min intervals over a 4-week period.
Partitioned into 78 clusters
Within a cluster:
  Tunnels fixed
  Link capacities change (partial/full link failures)
  250 unique link capacity configurations in some clusters
Across clusters:
  Tunnels change
    E.g., node/link addition
  20% of the last cluster’s tunnels not present in the first cluster
Time
Cluster 1
Cluster 2
Cluster 78
Past work has only evaluated on static topologies

## Slide 16
Can HARP work in dynamic environments?
Training: First three clusters
Validation: Next three clusters
Testing: 72 remaining clusters
Normalized MLU =
Optimal: MLU generated by clairvoyant LP. Only needed for plotting.
HARP is within 12% of optimality 98% of the time despite
significant tunnel and topology changes outside training set
Better

## Slide 17
HARP vs DOTE
Train and test on same cluster
On average, HARP’s MLU is 3x lower
DOTE assumes static link capacities
  Cannot handle partial/full link failures
Across clusters even more challenging

## Slide 18
Can HARP work with inaccurate predictors?
When the predicted matrix is used, HARP outperforms LP solvers by 9% on the 80% percentile.
Benefits with other predictors are even higher. See paper.
HARP learns to be robust to prediction errors.

## Slide 19
Preserving invariances with HARP
Tested on
Unshuffled Tunnels
Shuffled Tunnels
When tunnels in testing are shuffled relative to training:
  HARP retains its performance
  DOTE and TEAL generate 1.5x MLU
Better

## Slide 20
Importance of the aligned architecture
On average, HARP’s MLU is 1.6x lower than that of HARP_NoRAU

## Slide 21
Other Experiments
HARP’s ability to handle failures outside training set
  Full-link failures
  Partial-link failures
Computation times

## Slide 22
Conclusion
HARP: First neural TE scheme that can handle changing topologies
HARP is transferable across topologies
  Preserves key invariances to natural inputs transformations (e.g., reordering tunnels)
  Neural architecture is aligned to the optimization model
HARP outperforms classical LP solvers:
  5-13% lower average MLU based on traffic matrix predictor
  100x faster on large topologies
HARP performs well even with topologies/failures outside training data
  Close to optimal MLU in all cases
  34% lower MLU than DOTE and TEAL on average
We released HARP’s source code
https://github.com/Purdue-ISL/HARP